Study of Fuel Efficiency on Tug Boats With Use of Flowmeter Web Based Monitoring and Control System In P.T. X

# Danny Faturachman1, Achmad Djaeni2

# 1Department of Marine Engineering, Darma Persada University, Jakarta, Indonesia, fdanny30@yahoo.com,

# 2Department of Marine Engineering, Darma Persada University, Jakarta, Indonesia, a.djaeni@gmail.com

# ABSTRACT

In order to increase efficiency, a monitoring system has been doing for measuring operational performance existing.  After a system created and used, usually management can measure performance and take action anything to improve the efficiency. With all information that has been collected, management will be able to produce a decision accurate and take action to increase productivity and efficiency operational. P.T. X after implementing the installation of flow meters in all ships and have examined in research before, now deeper by applying the use of flow meters which  internet use web-based as a sensor long-distance, as to be monitored anytime and wherever with by use of a sensor equipment named eGenKit. For that the study is done to assess the use of fuel efficiency on tug boats with use web-based monitoring and control system in P.T. X.

Keywords: digital, eGenKit, flow meter, fuel oil consumption, tug boat.

.

# INTRODUCTION

All The measurement of the flow of fuel is very important in management process of fuel in a ship. An instrument for measuring the flow called flowmeter. This device serves to determine how much fluid required in the process of continuous and how a fluid in distributed, fluid referred to fuel oil in a ship. The measurement of fuel now is also intended for energy efficiency which was trying to managing and controlling the use of energy in their company that could have dividend more, so can increase cash flow to remain competitive in the market, give a bonus more to an employee and increase advantage to shareholders.

At the sea, energy sources for fuel must be managed, controlled and made more efficient. The cost of fuel is expenditure largest indispensable both on shipboard and in a building. Factors that have brought inefficiency fuel is: wrong design for ship (for example like the calculation size of propeller, machine, and others), a lack of competence crew especially that associated with operation and management, the theft of the fuel and the quickness supervisory to support operational especially times in dealing with the problems. In order to increase efficiency, a monitoring system to do for measuring operational performance existing. After a system created and used, usually management can measure performance and take action anything to improve the efficiency. With all the information that has been collected, management be able to produce a decision accurate and take action to increase productivity and efficiency of the operational problem.

P.T. X after implementing the flowmeters in all ships her and has examined in research before. From the research before (Danny, 2014) P.T. X group is a company that moves in information technology, resources, energy, mining logistic & services. P.T. X group owned company shareholder in systems integration, ranging from Information Technology business process outsourcing / employment, services logistician / carting, business oil and coal mining. One of subsidiary of P.T. X is company services provided sea transportation that focuses on sea transportation which includes a barge intensity and ship for transporting coal, ranging from dredging, loading-unloading until transporting. One large project of that company have established cooperation with the government for transporting coal to nuclear power plant (PLN) in Pelabuhan Ratu, West Java.

P.T. X have some of tug boat, a small vessel assigned to pull or push larger vessels in port. Besides the tug is also serves to draw barges contains coal which comes from treatment coal plant to be brought to the port place and after that carried out to the trucks. Now the research much deeper by applying the use of flowmeters using the internet use web based as a sensor remotely so could be monitored anytime and wherever with by use of a sensor equipment named eGenKit. That is why the study is done to assess the fuel efficiency on tug boat using executive web-based monitoring and control system in P.T. X.

# Problem Identification

The problems faced by P.T. X is:

- How to election the type of flowmeter which suitable for tug boat 2060 HP in this case there are two tug boats i.e. tug boat Titan 21 and Titan 23, with great vary fluctuations rpm machine;

- How to application installment in a ship adapted with spaces in an engine room and system fuel;

- How to monitor or analyzes the use of flowmeter has been consistent with the objectives of installment that creation for the use of fuel in a ship.

In this research, P.T. X developed the installation of flowmeter with use the web-based sensors so that can be controlled by the use of fuel wherever and anytime by using eGenKit. Sensors set to be fitted in each the ship is:

-- Fuel Consumption sensors 2 pieces those in the in-let and out-let, type sensors fuel-consumption is flow meters corilois owns by the Emerson , size 1/4 inch;

-- Bunker sensor 1 pieces to be installed in a pipe filling-bunker, type sensors bunker is flow-meter corilois owns by the Emerson, size 3 inch;

-- Rpm sensors 4 pieces, 2 in play engine (Main Engine) and 2 in Generator Set (Auxiliary Engine).

Figure 1. Flowmeter Diagram Analog and Digital System

Types of flowmeter:

Flowmeter discussed is the type rotary analog Aquametro brands and type digital corilois Emerson brands. Flowmeter type rotary analog Aquametro brands used only on system discharging fuel and not used on system filling bunker. The use of satellite system to report online only done on flowmeter type digital coriolis Emerson brands on system discharging fuel and also a system of filling bunker.

RESULTS AND DISCUSSION

- Research Location

The object previous studies located on the island of Batam to the construction of ships that uses eGenKit  there are two ships i.e. tug boat Titan 21 and 23. After that observation and data processing brought from location where the tug boat sailing was between port from Pelabuhan Ratu to Kotabani, Bengkulu.

Figure 3. Sailing between port Pelabuhan Ratu-Kotabani, Bengkulu

- History of Fuel Consumption per trip

Figure 4. History of Fuel Oil Consumption per trip

- Ship Fuel Oil Consumption

Table 1. All the Ship Fuel Oil Consumption

| Fuel Oil Consumption |
| --- |
| Name of the Ship | Actual | Target | Unit |
| TB.Titan 03/06 | 14,779 | 15,268 | Littre |
| TB.Titan 03/06 | 45,744 | 47,942 | Littre |
| TB.Titan 05/04 | 29,448 | 31,650 | Littre |
| TB.Titan 07/08 | 27,855 | 31,650 | Littre |
| TB.Titan 07/08 | 26,544 | 30,456 | Littre |
| TB.Titan 09/10 | 24,503 | 31,650 | Littre |
| TB.Titan 09/10 | 19,664 | 30,456 | Littre |
| Titan 70 | 39,435 | 60,000 | Littre |
| TB.Titan 11/12 | 52,923 | 52,734 | Littre |
| TB.Titan 13/14 | 45,223 | 52,734 | Littre |
| TB.Titan 15/16 A. | 31,411 | 31,650 | Littre |
| TB.Titan 15/16 B. | 30,166 | 31,650 | Littre |
| TB.Titan 17/18 | 44,555 | 52,734 | Littre |
| TB.Titan 19/20 | 51,293 | 52,734 | Littre |
| TB.Titan 21/22 | 27,434 | 30,456 | Littre |
| TB.Titan 23/24 | 29,620 | 30,456 | Littre |
| Average | 36,040 | 40,948 | Littre |

Figure 5. Graph of All the Ship Fuel Oil Consumption

- eGenKit Identification

eGenKit is a system based on monitor long-distance web-based and solutions to control and helps the company make a decision accurately to optimize its operation. eGenKit consist of:

a ) panel localized ( hardware ) to be fitted on board, and

b ) server centralized ( to store data and management ).

eGenKit does not require software which enable the user have access to the ship all the time and anywhere. eGenKit uses transmission data hybrid between GPRS and satellite to produce a data transmission cost cheaper and can coverage revenue thoroughly.

Figure 6. System Architecture of eGenKit

Figure 7. Login Page

Figure 8. Dashboard Display

- Fuel Oil Consumption of the Ship which Used eGenKit

Figure 9. Fuel Oil Consumption of Titan 21

Figure 10. Fuel Oil Consumption of Titan 23

CONCLUSION

- From the consumption of fuel can be seen there has been a target as follows:

| Titan 21 | Actual | Target | Unit |
| --- | --- | --- | --- |
| April | 31,503 | 31,620 | Littre |
| May | 27,034 | 31,620 | Littre |
| June | 27,434 | 30,456 | Littre |

| Titan 23 | Actual | Target | Unit |
| --- | --- | --- | --- |
| April | 34,974 | 31,620 | Littre |
| May | 33,606 | 31,620 | Littre |
| June | 29,620 | 30,456 | Littre |

- Will be conducted socialization in all ships on the target fuel efficiency, currently has been running in some ships and there are good reception from crew members of the ship.

- Furnish equipment for fuel-sensor, fuel-monitoring, fuel-security, including: equipment fuel-sensor package to new ship (Titan 25, Titan 27, Titan 29 and Titan 31), there are 3 choice, namely:

- eGenKit, package 1 flowmeter corilois and rpm censorship, GSM transmitter,

- Broil, package 4 flowmeter oval-gear and rpm censorship, GSM transmitter.

-  Aquametro, package 4 flowmeter rotary and CCTV rpm + GSM CCTV transmitter.

# REFERENCES

- Aqua Metro Contoil Fuel Oil MeAters, Istec Corporation.

- Arifin, Zainal Rabiman, Sistem Bahan Bakar Motor Diesel, Yogyakarta, Graha Ilmu, 2011.

- Artono Koestoer, Raldi, Pengukuran Teknik, Jakarta, Departemen Teknik Mesin Fakultas Teknik, Universitas Indonesia.

- P2M, Diktat Dasar-dasar Pengukuran dan Kesalahan Pengukuran, Fakultas Teknik, Universitas Indonesia.

- Tomo, R. Choerniadi, Menelusuri Teknologi BBM Perkapalan dan Aplikasinya, Jakarta, PT. Bunda Mulia Abadi Jaya, 2013.